## Slide 1
Karl Reich, Ph.D.
Independent Forensics
Lombard IL
A New and Better Forensic Test for
Human Semen

## Slide 2
Introduction to Independent Forensics
5,600 sq ft of combined laboratory and office space
Suburban Chicago – 18 minutes from O’Hare
– 30 minutes from The Loop
Laboratory personnel: MS and Ph.D. scientists
Contract R & D
Products for Forensic
Laboratories
Forensic DNA laboratory
Accreditations: ISO 17025, NY-DOH, AABB, CLIA
Specialize in LCN / Trace Protocols
Profiles from < 0.1 ng

## Slide 3
RSIDTM – Rapid Stain IDentification
Developed under R & D contract
Requirement: Confirmatory tests for:
Current Tests: presumptive
cross-reaction – species and body fluids
non-specific – other conclusions possible
widely used – SOPs, report guidelines
Jennifer Old,
Liz Graffy,
Brett Schweers,
Karl Reich,
&
Others . . . . . . .
Brought to you by:
SALIVA
SEMEN
BLOOD
URINE

## Slide 4
Introduction to RSIDTM
Tests for Forensic Laboratories
Lateral Flow Immunochromatographic
Strip Tests for the
Identification of Body Fluids
RSIDTM - SEMEN

## Slide 5
Test Format: Lateral flow immunochromatographic strip test
Antigen Detected: Human Semenogelin (Sg)
Antibodies: 2 Mouse monoclonals, non-overlapping epitopes
Labeling: Colloidal Gold
SEMEN
Sensitivity: < 1 l semen [ slight Hook effect observed]
Cross-Reaction: None observed to date (see list)
Test Read-out: Visual
Assay Time: 10 minutes ‘active’ time

## Slide 6
SEMEN
~ 15 min
RSIDTM
Running Buffer
mix aliquot of extract
with running buffer
add to RSID-Semen
adsorb stain onto swab
or
remove cutting
extract in provided
extraction buffer
or
or

## Slide 7
B/Se/U
Body Fluids
B/Se
Sa/U
Semen
0 l
1 l
5 l
25 l
100 l
Extract
50 l
semen
extracted in
1 ml
SEMEN
Semen
0 l
50 nl
250 nl
1.25 l
5 l

## Slide 8
SEMEN

## Slide 9
SEMEN
Efficient: Assay procedure integrated in DNA-STR analysis
Fast: Results in 10 minutes post stain extraction
Sensitive: Detects 50-100 nl of human semen
– stated detection limit: 1 l
No observed cross reaction with other body fluids,
domestic animals,
exotic species,
body fluid mixtures
First Confirmatory Test for Human Seminal Fluid

## Slide 10
Questions
Comments
Samples
Gripes
Karl Reich
Tel 708.234.1200
Fax 708.978.5115
karl@IFI-test.com
www.IFI-test.com